## Slide 1: EE 123: Bioelectricity
Fall 2020
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Bioelectricity I – intro

## Slide 2: Big picture of the course
Where does bioelectricity come from?
Neurons and working with the nervous system
Cardiac bioelectricity
Worms

## Slide 3: Do we care about this?
Argument for no
  Some people think biological physics is the best; others go into sleep mode 
  Wide range of backgrounds
  Can design things without understanding the physics
Argument for yes
  People who understand details in multiple aspects are valuable
  bioelectricity and electroceuticals are a newly-growing field; it’s hard to predict where it will be in 10 years
  The fundamentals of bioelectricity won’t change
Resolution
  Backgrounder + quiz for people without background
  Distill it down to a few equations & models → you can get by

## Slide 4: In the news…
https://spectrum.ieee.org/the-human-os/biomedical/devices/using-weak-electric-fields-to-make-viruskilling-face-masks
How do N95 masks use electrets?
You can:
  Do a very brief read, and then chat about it with me during office hours
  Do a more detailed read, and then talk about it for the quiz on this unit

## Slide 5: Outline for this section
Primer on Q, I, V, C (charge, current, voltage, capacitance)
Diffusion current ()
Drift current (jdrift = kVmem)
Diffusion + drift = Nernst ()
Ion pumps
Electrical model of a cell (jtotal,Na = gNa (Vmem-VNNa) + jpump,Na)

## Slide 6: Electric charge
So what is electricity, anyway?
Start with the basics: charge.
  Atoms have electrons (negative charge) and protons (positive charge)
  Same number of each → net zero charge
  An atom can give away an electron to another atom
  The “giver” then has one more proton than electron → net charge of +1
  The receiver has net charge of -1
  Both are now called ions
  Example: NaCl → Na+ and Cl-
11 protons
11 e-
Na
17 protons
17 e-
Cl
10 e-
18 e-
Na+
Cl-

## Slide 7: Electric force
+ and - ions attract each other
  Like there’s a big invisible rubber band between them
  You pull them apart & they go back together!
Two positive ions (or two negative) repel each other
  Push them together & they run away
  That’s pretty much what charge is
“Coulomb’s Law” says how hard they push and pull
  We’ll get quantitative soon enough
  The unit of charge is a “Coulomb” (named after Charles-Augustin de Coulomb)

## Slide 8
Opposite charges attracting
Na+
Cl-

## Slide 9
Two positive charges repel
Two negative charges do too
K+
Na+

## Slide 10: Work can overcome this
Two positive charges repel
Na+
Na+

## Slide 11: Fixed and movable charges
Why are the Na+ and Cl- stuck?
  who knows, it’s just an example
  maybe there’s a cell membrane between them, with an ion channel that’s permeable to K+ but not to Na+ or Cl-
What will happen?
  The movable K+ will travel to the right
Na+
Cl-
these charges are stuck in place
K+
this charge is movable
cell interior
Notes: Give a two-sentence description of what’s a cell & an ion channel.

## Slide 12: Fixed and movable charges
Again, we can move it back with enough work
Na+
these charges are stuck in place
K+
this charge is movable
cell interior
Cl-

## Slide 13: Voltage
We could work with Coulomb’s Law to compute forces, accelerations and velocities
But it’s usually easier to use a higher-level concept – voltage
In fact, we won’t learn Coulomb’s Law
  but it was still useful to learn about positive & negative ions!

## Slide 14: Voltage
K+
What if we had twice as many fixed-in-place ions?
  There would be twice as much electric force on the K+
  it would move twice as fast
  it would require twice as much work to move it back
Any time you separate charges, you get a voltage
Separating charges across a cell membrane is the basis of bio-electricity
Voltage is the amount of energy (or work) needed to push 1C of charge across from point A to point B
  The unit is Volts
  1C of charge, moving across 1V, takes 1J of work
  2C of charge, moving across 3V, takes 6J of work
Na+
Cl-
these charges are stuck in place
K+
Na+
Cl-
this charge is movable

## Slide 15: Voltage
K+
Separating charges across a cell membrane is the basis of bio-electricity
The fixed separated charges (Na+ and Cl-) create, e.g., 3V
A Volt is a Joule/Coulomb
  moving (e.g.,) 2C of K+ across 3V takes how much work?
Next question: why did the Na+ and Cl- create 3V and not 4V?
How much voltage gets made by how much separated charge?
Q=CV
Na+
Cl-
these charges are stuck in place
K+
Na+
Cl-
this charge is movable
how much charge: e.g., 1 Coulomb
how much voltage: like, 3 Volts
Capacitance of the cell membrane (mostly, how thick it is). In this case, .33 Farads
=6 Joules

## Slide 16: Current
Say we have an observer (that’s the eye!) sitting in the middle and counting how many ions pass by
  the number of ions that pass by every second is called current
  the current per m2 of cross-sectional area is called flux
  the unit of current is an Ampere (from André-Marie Ampere)
  1 A ≡ 1 C/s
What are the units of flux?
  A/m2
Na+
Cl-
K+

## Slide 17: End of electricity primer
That’s electricity in a nutshell.
  It’s very useful for everything from washing machines to cell phones.
  And…most cells in our body create voltage
The big takeaways:
  Intuitively, what is charge, voltage, current and flux
  Opposite charges attract, like charges repel
  Q=CV

## Slide 18: Outline for this section
Primer on Q, I, V, C
Diffusion current ()
Drift current (jdrift = kVmem)
Diffusion + drift = Nernst ()
Ion pumps
Electrical model of a cell (jtotal,Na = gNa (Vmem-VNNa) + jpump,Na)

## Slide 19: Diffusion
“(In the nanoworld), everything is dancing,” Philip Nelson, Biological Physics
Particles move randomly; on average, they move from high concentration to low concentration

## Slide 20: Diffusion
Intuition:
  Assume particles move in random directions
  On average more particles cross the membrane right→left than left→right
  It is probabilistic, but deterministic if there are enough particles
  The magic of statistical mechanics!
Cell
ECF
cell membrane
how big the gradient is
how fast ions cross the membrane
Note the sign: diffusion evens out concentrations
Units:
magic constant
Notes: The diffusion story: Richard Brown, Brownian motion, saw pollen move around in a vial with a microscope (1827). Assumed the pollen was alive. Stuck the vial in a dark room for a year – still moved around! Several similar experiments, including: Took flecks of stone from the Giant Sphynx and dropped them in water – they moved too! Einstein finally explained it in 1905.

## Slide 21: What is D, really?
We have a simple equation
We (hopefully) know what it means
D is how fast an ion moves, for a given gradient pushing it
What affects D, our magic proportionality constant?
  High-volume ion:
  In a vacuum:
  In a liquid
will bump into lots of things and slow down, so D will be small
D will be quite large (not relevant for us!)
Not nearly so large

## Slide 22: Example
If D=.1 m2/s, then what is the flux?
  Negative sign means ions are moving to the left
After enough time, what will happen?
  The right-side space will go empty and the left-side will have all the ions?
  They will equalize? If so, why?
Cell
1 ion/m3
ECF
3 ions/m3
dx = 1
time
3
1
concentration
Will they always eventually equalize to 2 moles/m3
  No. E.g., if the ECF is really big then they will equalize to just under 3
  Thought question: is the ECF usually really big?
Notes: Note that diffusion is really a partial differential equation; the “flux” part is really d[Na]/dt. We’ve simplified the d/dx by assuming d[Na]/dx is 0 in the cells and constant in the membrane

## Slide 23: Example
Assume the ECF is big, the cell is really little
After diffusion is done…
Why? At any time,
  # of ions leaving the ECF = # entering the cell
  So [ion] changes faster in the cell than in the ECF
dx = 1
time
3
1
concentration
ECF
3 ions/m3
Cell
1 ion/m3
ECF
2.99 ions/m3
Cell
2.99 ions/m3
An analogy:
  It’s 20° outside, your house is 70°, and you open the door
  After a few hours your house is also 20°, and you’ve not appreciably warmed up the earth

## Slide 24: Outline for this section
Primer on Q, I, V, C
Diffusion current ()
Drift current (jdrift = kVmem)
Diffusion + drift = Nernst ()
Ion pumps
Electrical model of a cell (jtotal,Na = gNa (Vmem-VNNa) + jpump,Na)

## Slide 25: Drift
We saw diffusion
  random thermal motion + concentration gradient = net ion currents
Drift:
  charged ion + voltage pushing it around = ion current

## Slide 26: Drift current
We said similar charges repel, opposite charges attract
  That causes charges to move
  We call this drift current
Problem: real systems have too many charges to deal with 
More common formulation:
  The separated charges (Na+ and Cl-) create a voltage
  The voltage creates a K+ drift current (or flux)
Na+
Cl-
these charges are stuck in place
K+
Na+
Cl-
this charge is movable

## Slide 27: Separated charges create a voltage
Separating charges across a cell membrane is the basis of bio-electricity
The fixed separated charges (Na+ and Cl-) create, e.g., 3V
Why did the Na+ and Cl- create 3V and not 4V?
How much voltage gets made by how much separated charge?
Q=CV
Na+
Cl-
K+
Na+
Cl-
this charge is movable
these charges are stuck in place
how much charge: e.g., 1 Coulomb
how much voltage: like, 3 Volts
Capacitance of the cell membrane (mostly, how thick it is). In this case, .33 Farads
+ 3V -

## Slide 28: Cool tricks to do with voltage
K+
Separating charges across a cell membrane is the basis of bio-electricity
The fixed separated charges (Na+ and Cl-) create, e.g., 3V
A Volt is a Joule/Coulomb
  moving (e.g.,) 2C of K+ across 3V takes how much work?
Voltage tells you how much work it takes to move an ion from one place to another
Na+
Cl-
K+
Na+
Cl-
=6 Joules
Warning – we won’t use this fact in this course (but it’s what voltage really is)
+ 3V -

## Slide 29: Cool tricks to do with voltage
Ohm’s Law: V=IR or I=V/R
  /k
Voltage tells you how much drift flux you get
Is /k the same as I=V/R?
  j is a flux (C/m2∙s) ; I is a current (C/s)
If Ohm’s Law tells us jdrift, why do we need ?
  Drift and diffusion are two different reasons ions move around
  Metal wires don’t really have diffusion; all we need is Ohm’s Law
  Ions in a liquid have both types of currents!

## Slide 30: Why does Ohm’s Law work?
Drift flux
Intuition:
  qion V / L → how hard you’re pushing (N)
  μion → mobility; how easy the ion is to push (m/s per N)
  put them together → how fast each ion moves (m/s)
  [ion] → how many ions there are (density of ions/m3)
  And it’s all nice and linear… at least to a first order
  Units:
  This is just the quantitative version of charges attracting/repelling
Ohm’s Law: V=IR or I=V/R
  /k
mobility
pushing force (attract/repel)
ion density
Backup

## Slide 31: qionV/L → force: why?
We said
  And said qion V / L → how hard you’re pushing (N)
We previously said same(opposite) charges repel(attract)
Coulomb’s Law connects these two statements
Backup

## Slide 32: qionV/L → force: why?
Coulomb’s Law:
  force between two particles is
Equivalently:
  one ion creates an electric field
  an electric field action on a charge creates a force f=qE
A bit of math: is really div·E = ρ/ε
Voltage is defined by gradient(V) = -E
  in 1 dimension, E = -dV/dx
+++++
- - - - -
The above two equations can derive that E=V/L, and Q=CV, and even the value of C
Maxwell’s 1st eqn
Backup

## Slide 33: qionV/L → force: why?
A basic statement of electric charges
f=qE
A charge q
in the presence of a field E
feels a force f
Newton’s first Law
  acceleration a = f / m = qionE/mion
  Constant E field implies constant acceleration
  Will the ion travel faster and faster until it goes infinitely fast?
Not really
  First, nothing ever goes infinitely fast 
  Einstein said relativity gets in the way
Backup

## Slide 34: Mobility*force = velocity – why?
Car with your foot on the gas (providing a constant force)
What stops your car from hitting 10K mph?
  Air drag.
  The faster you go, the more drag, until it all balances out
Ions see the same drag forces
  Car bumps into random air molecules
  An ion bumps into other ions & molecules
End result: v = μion f = μion qion E
Intuition:
  More charge or field → more force → more speed
  More V → more E
  And it’s all nice and linear… at least in our simple model
And then Jdrift = v[ion]
mobility
velocity
Backup

## Slide 35: Mobility*force = velocity – why?
We have a simple equation
We (hopefully) know what it means
What affects μ, our magic proportionality constant?
High-volume ion:
In a vacuum:
In a liquid:
The units work
  f=qE: E is N/C, q is C and so E q is N
  v= μf: μ is m/s per N, so μ f is a velocity
will bump into lots of things and slow down, so μ will be small
μ will be quite large (not relevant for us!)
Not nearly so large.
Backup

## Slide 36: Mini quiz
Can you explain, in a few sentences, what diffusion is?
Can you explain, in a few sentences, what drift is?
Can you explain the letters in the equation
Can you explain the letters in the equation I=V/R?
What are the units on flux?

## Slide 37: Outline for this section
Primer on Q, I, V, C
Diffusion current ()
Drift current (jdrift = kVmem)
Diffusion + drift = Nernst ()
Ion pumps
Electrical model of a cell (jtotal,Na = gNa (Vmem-VNNa) + jpump,Na)

## Slide 38: Dilemma
Diffusion – particles move from high concentration to low
  End result: uniform concentrations everywhere
  Same amount of Na+ on inside & outside of cell
Drift is caused by voltage
  Voltage is caused by separated charges
  E.g., lots of Na+ inside and lots of Cl- outside
But…
  If all particles are uniformly distributed, how can we have separated charges?

## Slide 39: Drift + diffusion = voltage
Cell membrane
intra-cellular fluid
extra-cellular fluid
Cell
Protein
Cells make lots of proteins
Protein → big negative piece + small positive piece
P-
P+

## Slide 40: Drift + diffusion = voltage
Cell interior is charge neutral
So is the ECF
P-
P+
Any voltage?
Any diffusion across the cell membrane?
  Assume P+ can get through the membrane, but P- is too big
P-
P-
P-
P+
P+
P+
Notes: No separated charge, so no voltage
But there is diffusion of P+

## Slide 41: Drift + diffusion = voltage
P+ diffuses out of the cell
Is there any voltage?
  ICF is negative, ECF is positive
P-
P+
Which direction does P+ diffuse?
Which direction does it drift?
With only one P+ outside, V is small: diffusion > drift
P-
P-
P-
P+
P+
P+

## Slide 42: Drift + diffusion = voltage
More P+ diffuses out
More separated charge
More voltage
P-
P+
Eventually we reach equilibrium
  All the P- is still stuck inside
  Diffusion current out = drift current in
Next question – what is V at that point?
P-
P-
P-
P+
P+
P+

## Slide 43: Nernst equation
Well-known equation
  required by doctors to pass their boards!
Assume:
  At any point in space, drift + diffusion = 0
  I.e., equilm, no net current
A little calculus gives:
This is called a Nernst voltage
How can we use it?
  If we know, e.g., [Na]int and [Na]ext then we know Vmem!
  We’ll use it very soon

## Slide 44: Nernst assumptions
The big assumption: drift = diffusion
Why might that be true?
Biology is full of machines that create homeostasis
  Maintain your body temp at 98.6°
  Maintains chemical concentrations quite steady
  Every flux leaving a cell is balanced by one entering
Drift and diffusion are “often” balanced at homeostasis
  But not always
  We’ll see why pretty soon, and make this more precise

## Slide 45: Giant squid voltages
The membrane has ion channels
  little holes in the cell membrane that ions can diffuse through (aided by molecular machines)
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
intra-cellular fluid
extra-cellular fluid
Remember: Pr- cannot cross the cell membrane
Minor problem: K+, Na+, Cl- cannot either!
So how can diffusion, drift happen?

## Slide 46: In-class exercise
Compute ΔV for Na, for K and for Cl
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
intra-cellular fluid
extra-cellular fluid
Is ΔV the same for Na, K and Cl?

## Slide 47: Nernst derivation
Assume:
  At any point in space, drift + diffusion = 0
  I.e., no net current
Derivation:
  drift flux =
  diffusion flux =
  So
Einstein relation says D = μ kT
Backup

## Slide 48: Outline for this section
Primer on Q, I, V, C
Diffusion current ()
Drift current (jdrift = kVmem)
Diffusion + drift = Nernst ()
Ion pumps
Electrical model of a cell (jtotal,Na = gNa (Vmem-VNNa) + jpump,Na)

## Slide 49: In-class exercise
57mV
-78mV
-62mV
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
intra-cellular fluid
extra-cellular fluid
Is VNernst the same for Na, K and Cl?
No!
But if VNernst is the ΔV across the cell membrane, it can only have one value ?!?

## Slide 50: Forces on the system
First force: diffusion (our old friend)
Which way does diffusion flow for K+, Na+ and Cl-?
  K+ out; Na+ and Cl- in
intra-cellular fluid
extra-cellular fluid
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM

## Slide 51: Results of diffusion
If diffusion happen long enough and there is no drift, what will happen to the concentrations [K+], [Na+] and [Cl-] inside vs. outside of the cell?
  For each ion, the concentration inside and outside the cell will eventually become equal
This is not what actually happens!
  As we’ve explained, there is drift
extra-cellular fluid
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM

## Slide 52: Drift currents
In fact, the cell stabilizes to Vmem ≈ -60mV
  (given the amount of unbalanced charge, and Q=CV)
  This voltage will push the ions around, as we’ve discussed
  Which way do drift currents flow?
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
Blue arrows = diffusion
Green arrows = electric current
--- +++ 60mV

## Slide 53: Nernst sanity check
First look at Cl-. Can drift and diffusion currents balance?
  Yes; drift current out, and diffuses in
  VClNernst = -62mV  Vmem. Cool!
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
Blue arrows = diffusion
Green arrows = drift current
--- +++ 60mV

## Slide 54: Nernst sanity check
Next look at K+. Can drift current and diffusion balance?
  Yes; drift current in, and diffuses out
  VKNernst  -78mV
  Not quite right ?!?
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
Blue arrows = diffusion
Green arrows = drift current
--- +++ 60mV

## Slide 55: Nernst sanity check
Finally, look at Na+. Can drift current and diffusion balance?
  No – they both flow inwards!
  VNaNernst  +57mV
  Not even close ?!?
What’s going on here?
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
Blue arrows = diffusion
Green arrows = drift current
--- +++ 60mV

## Slide 56: Another ion-flow source
Drift and diffusion currents do not balance
  another molecular machine at work: ion pumps
Ion pumps pump 3 Na+ out and 2 K+ in
  Na+ flows in (drift & diffusion currents) through ion channels, and gets pumped right out again (inward and outward flows balance at steady state)
  K+ flows in from drift current and is also pumped in; diffusion out exactly balances this total inwards flow
Why was Cl- the only ion whose VNernst exactly matched the cell voltage?
  There is no Cl- pump
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
other-=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
Blue arrows = diffusion
Green arrows = drift current
Red arrows = ion pump
--- +++ 60mV
3Na+
2K+

## Slide 57: Steady state
Steady state: all concentrations and rates are unchanging over time
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
P -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
Blue arrows = diffusion
Green arrows = drift current
Red arrows = ion pump
--- +++ 60mV
3Na+
2K+
diffusion in = drift out
diffusion in + drift in = pump out
diffusion out = drift in + pump in
No net flow in/out
concentrations unchanging
flow rates unchanging
We are at steady state
Nernst is only true for Cl
  Cl:
  Na:
  K:

## Slide 58: Where are we?
We learned what drift and diffusion are
When drift = diffusion, Nernst is true and we know Vmem
But for a cell, that’s only true for Cl
  The cell is at SS
  Nernst is not true for Na, K
  Clearly the cell “works;” it can stay at SS essentially forever
Our nice Nernst formula doesn’t always work
  Now we know why – but we still have a problem
  How do we model/analyze a cell?

## Slide 59: Definitions
Define some terms:
  detailed balance: every forwards reaction is balanced by a reverse reaction
  equilibrium: everything is unchanging over time, and no energy is being expended
  steady state: all concentrations and rates are unchanging over time. Energy can be expended.
Nernst is true
You are dead
You are alive
Nernst is false
Ion pumps require energy
Steady state doesn’t imply detailed balance
  and thus does not imply Nernst
Na, K pumps run
Cl has no pumps
Nernst is true
Backup
Notes: This is partly a backup slide. The important thing is not the definitions of detailed balance, equilm and steady state (though we will use those terms, and redefine them each time). Really, the important thing is the notion that pumps break Nernst.

## Slide 60: Outline for this section
Primer on Q, I, V, C
Diffusion current ()
Drift current (jdrift = kVmem)
Diffusion + drift = Nernst ()
Ion pumps
Electrical model of a cell (jtotal,Na = gNa (Vmem-VNNa) + jpump,Na)

## Slide 61: Modeling diffusion in a cell
Simplifying assumptions:
  Cell concentrations change very slowly over time
  Assume they’re pretty much constant
So diffusion flux is… a constant!
Our model is really simple 
  jdiff,Na = constant
It’s only constant for a given set of concentrations!
If [Na] changes over time, then so does jdiff,Na
Because the ion channels are small compared to cell volume

## Slide 62: Modeling drift in a cell
Use Ohm’s Law
  jdrift,Na = Vmem / RNa
  jdrift,Na = gNaVmem (where gNa≡ 1 / RNa)
GNa is conductance of Na ion channels

## Slide 63: Modeling the ion pumps
The pump is even easier
Call it constant fluxes jpump,Na and jpump,K
Not quite so simple in real life:
  it pumps faster if you put more fuel (ATP) in
  it pumps slower if it’s fighting a big gradient
  We’ll ignore both issues

## Slide 64: Simple equation
jtotal,Na = jdiff,Na + gNaVmem + jpump,Na
= gNa (Vmem + (jdiff,Na/gNa)) + jpump,Na
  This is reasonably simple, but we can do even a bit better
Ignore the pump for a moment
  We know that, without pumps, diffusion and drift balance (i.e., no net flux) at the Nernst voltage
So a revised equation:
Is this surprising?
  The units work, of course
  We know that Vmem * gNa = jdrift,Na , which must equal jdiff when V=VNNa. So it’s not at all surprising
This is bioelectricity in a nutshell! Does it make sense?
jtotal,Na = gNa (Vmem - VNNa) + jpump,Na

## Slide 65: What the model says
jtotal,Na = gNa (Vmem - VNNa) + jpump,Na
There’s a separate model for each ion. Cl doesn’t have a pump
Main input: Vmem
Output: flux (how fast the ion is entering the cell)
VNNa and jpump,Na depend on [Na]
Hidden input: [Na]int
And [Na]ext is usually assumed constant
There’s only one Vmem, shared by all ions
Drift
Diffusion
How many ion channels there are
Notes: Any reason why Vnernst might represent diffusion? Because it’s proportional to [out]/[in]!

## Slide 66: Modeling our cell as a circuit
A current source simply provides a constant current
ICF
77mV
-89mV
-71mV
GNa
GK
GCl
jNa
jK
ECF
Vmem

## Slide 67: Modeling our cell as a circuit
A voltage source (a.k.a. a battery) simply provides a constant voltage
77mV
-89mV
-71mV
ICF
GNa
GK
GCl
jNa
jK
ECF
Vmem

## Slide 68: Modeling our cell as a circuit
A resistor operates according to Ohm’s Law: I=V/R (or I=GV with G1/R)
77mV
-89mV
-71mV
ICF
GNa
GK
GCl
jNa
jK
ECF
Vmem

## Slide 69: What to do with our model
We can build a simulator (BITSEY)
  flux tells us how fast the concentrations are changing
  If there are 2 moles of Na in the cell, and a flux of .3 M/second entering, then if we simulate for 1s
  there are now 2.3 moles of Na.
  A simulator just does this over and over (each time computing new jdiff, g and VN for the new [Na]
We said that total charge in the cell determines Vmem (Q=CV)
  So our simulator will also tell us Vmem over time
Run the simulator until things stabilize
  Then we’ve computed the steady-state Vmem for a cell
  In fact, that’s Lab #2
Simulate short transients around steady state
  that’s how neurons work

## Slide 70: Done with the basics!
The main part of bioelectricity is done 
  But we haven’t built anything yet 
What’s coming next:
  lab #1 (Skittles diffusion) is hopefully a bit fun
  lab #2 (simple Bitsey) solidifies what we’ve learned
  add a few more details (QSS) and build a neuron
  add one more detail (GJs) and build cardiomyocytes
  build worms
But the hard part is done 

## Slide 71: Mini quiz
Can you explain the letters in the equation ?
Why doesn’t the Nernst equation work for Na or K in a cell?
Can you explain the pieces of the model below?
77mV
-89mV
-71mV
ECF
GNa
GK
GCl
jNa
jK

## Slide 72: BACKUP

## Slide 73: Start of Lab #2
Start Lab #2 in class
  Learn about Bitsey
  Run the 5-second simulations
Then run the long simulations at home

## Slide 74
Material to potentially be taught by the EEs:
  Draw the model as an equivalent ckt that has V & R for Na & K, R for Cl.
  Show how it reaches a final voltage
  Show how changing each R affects the voltage (for lab #1)
77mV
-89mV
-71mV
ECF
ICF
GNa
GK
GCl
INa
IK

## Slide 75: Ions in a giant squid
Observation: ICF and ECF each have high ion concentrations, but are roughly charge neutral
  Consequence: a small charge flow can greatly change the net charge
  and hence the net voltage
That’s what allows our nervous system to react quickly
[K+]=400mM
[Na+]=50mM
[Cl-]=52mM
Pr -=408mM
[K+]=20mM
[Na+]=440mM
[Cl-]=560mM
other+=110mM
intra-cellular fluid
extra-cellular fluid
Q = CV
Notes: If we had Q=100 C, then a ΔQ of 1C would make only a 1% change in Vmem. But if Q=1 C, then the same ΔQ doubles Vmem

## Slide 76: Inaccuracies
The model is not perfectly accurate
Our basic equations for drift and diffusion are correct
But we made big assumptions in applying them
  Diffusion: we assumed that the diffusion gradient is just a number – i.e., that it’s constant across the membrane
  I.e., that [Na] varies linearly across the membrane
  For drift, we assumed that [Na] was constant across the membrane Clearly both cannot be true!
Another model, Goldman-Hodges-Katz (GHK), is more accurate. Bitsey uses GHK to model ion channels
potential final project

## Slide 77: Our model is imperfect
“All models are wrong. Some are still useful,” George Box
Our model had a hidden input [Na]int
  The model only works at that [Na]int
  But the model is still “reasonably” good if we’re “reasonably” near that [Na]int
  We must re-compute g, VN and jpump when [Na]int changes substantially
Most important
  simple model = intuitive
  helps us to understand how cells behave
jtotal,Na = gNa (Vmem - VNNa) + jpump,Na